Modern Building	HS002 sample solution

Math Domain

| Number/Quantity | ( | Shape/Space |
| --- | --- | --- |
| Function/Pattern |
| Chance/Data |
| Arrangement |

Math Actions (possible weights: 0 through 4)

|  | 3 | Modeling/Formulating | 0 | Manipulating/Transforming |
| --- | --- | --- | --- | --- |
|  | 2 | Inferring/Drawing Conclusions | 2 | Communicating |

Math Big Ideas

|  | ( | Scale | ( | Reference Frame | ( | Representation |
| --- | --- | --- | --- | --- | --- | --- |
| Continuity |
| Boundedness |
| Invariance/Symmetry |
| Equivalence |
| General/Particular |
| Contradiction |
| Use of Limits |
| Approximation |
| Other |

1.	View of the building seen from the west (scale : 1 inch to 15 feet) is on the next page.

2.	View of the building seen from the south (scale 1 inch to 60 feet):

Figure for 1.

3a.	To calculate the distance between points D and E using the drawing from 2:

on the scale: 1 inch to 60 feet

The distance DE on the actual building is 80 feet.

To calculate the distance between points D and E using the drawing from 1:

on the scale: 1 inch to 15 feet

using the side view on a scale of 1 inch to 30 feet :

on the scale: 1 inch to 30 feet

.

3b.	Calculation of the distance between D and J from the top view:

(from the side view)

3c.	Calculation of the distance between E and J:

(from the simplified drawing)

.